## Slide 1: Secret Door Bookcases

## Slide 2: Why Secret Door Bookcases?
Conceals a room or closet-a form of security
Creates Useful Space from a Doorway
They Are Fun!
Not Always a bookcase-spice racks, tie and belt racks, mirrors, ticket booth and flat wall panels

## Slide 3: Two Types- “Innie” and “Outie”
Inward swinging doors are easier to conceal with molding
Inward 90 degree swing must account for thickness of door
Best is 180 degree swing-clears entire opening
Outward swings into the room you are standing in
Much harder to conceal-molding or hinges become visible

## Slide 4: Inward Swinging Door

## Slide 5: Inward Swinging Door Drawing

## Slide 6: Outward Swinging Door

## Slide 7: Types of Pivots
Door Hinges-heavy duty ball bearing commercial
Soss hinges
Piano hinges-knuckle is visible
Pivots-one upper, one lower. Difficult to install on concrete floors, tricky to adjust
Type of pivot must be able to carry hundreds of pounds
Hinges must usually be secured to house frame, not jamb

## Slide 8: Double Sided Door Kitchen-Study

## Slide 9: Narrow Doorway

## Slide 10: Narrow Doorway Installed

## Slide 11: Gun Closet

## Slide 12: Single Pivot Outward Swinging Door

## Slide 13: Structure-Casework
Racking under load
Badly built or installed will break or scratch the floor
Bookcase carcass is double strength

## Slide 14: 90 Degree Inward Swing

## Slide 15: 90 Degree Partial Open

## Slide 16: 90 Degree Full Open

## Slide 17: 180 Degree Door

## Slide 18: 180 Degree Partial Open

## Slide 19: 180 Degree Door Fully Open

## Slide 20: 180 Degree Door From Inside

## Slide 21: Shoe Storage

## Slide 22: Pullout Shoe Drawer

## Slide 23: Shoe Storage

## Slide 24: Shoe Storage Open

## Slide 25: Structure-Jamb
Bevel the jamb, not the case-less visible
Bevel is huge with 10” deep door
If you will see both sides of the door, may cover the gap with molding attached to the door
May extend wall to depth of door- 10” wall instead of 4”
Typically hinges on “innies” need to be at the back of the case

## Slide 26: Bookcase Hinged Mid Side

## Slide 27: Closures
Ball Catches
Magnets
Velcro-typically used for panels removed only occasionally
Locks-panic rooms. Simple pin can work.

## Slide 28: Installation
Tricky to install
Often make an exact scale template to locate jamb, hinge
Usually secure to wall framing
May need to extend wall on hinge side
Must be plumb and level in 3 axis
Mount to minimize gap at floor-target 1/8”
Plan for helper-very heavy casework
Install catch last

## Slide 29: Non-Bookcase Secret Doors
Shallow kitchen cabinets-spice racks
Mirror
Tie/Belt Rack
Ticket Booth
Flat Doors or Panels
Cabinets that move-Fridge cabinet, entertainment center

## Slide 30: Hidden Panel Doors

## Slide 31: Hidden Panel Doors Open

## Slide 32: Ticket Booth

## Slide 33: Ticket Booth Open

## Slide 34: Master Closet

## Slide 35: Mirror Door

## Slide 36: Tie and Belt Rack

## Slide 37: Tie & Belt Rack Open

## Slide 38: Cabinetry With A Secret
Cabinetry can change or conceal an opening
Cabinetry can look built in but actually move

## Slide 39: Non-Opening Façade Around Wine Cooler

## Slide 40: Fridge Cabinet Slides Forward

## Slide 41: Examples of Work
Hardwood Products Showroom
Client Kitchen Spice Rack
Client Bookcases concealing gun rooms or safes
Client Bookcase conceals stairway
Client Understair Shoe Rack Swings to Access Storage